## Slide 1: Dissemination of an SI-traceable optical frequency at 1572 nm using the Swiss academic fiber network
D. Husmann 20.01.2022
Searching for New Physics at the Quantum Technology Frontier
Workshop January 2021

## Slide 2: SNSF Sinergia: Precision molecular spectroscopy Project start: 2019; Project end: 2022
Precision molecular spectroscopy using a network for distribution of the Swiss primary frequency standard



Aim
Use frequency standard at METAS (atomic clocks) …
… to provide improved reference for precision molecular spectroscopy in University of Basel and ETH Zurich …
… by the means frequency dissemination over optical fibers …
… using the Swiss academic network provided by SWITCH.
Contribute to the international effort in high accuracy frequency dissemination and comparison
Système international d’unités
Frequency Metrology
Rydberg atoms
(F. Merkt)
Molecular ions
(S. Willitsch)
Sinhal et al. Science, https://doi.org/10.1126/science.aaz9837

## Slide 3
Theodor W. Hänsch – Nobel Lecture. NobelPrize.org. Nobel Prize Outreach AB 2021. Tue. 5 Oct 2021. https://www.nobelprize.org/prizes/physics/2005/hansch/lecture/
https://www.bipm.org (CC BY-ND 2.0)
Système international d’unités
: Transition between the two hyperfine levels of the unperturbed ground state of the 133Cs atom.
SI-traceability:
measurement trace to a realization of the second, with known uncertainty

## Slide 4: How to measure a frequency/time signal?
Compare it to a reference of equal or superior stability and accuracy
  Mechanical watch  train station watch
  Radio clock  GPS / Radio signal
  Kitchen oven  50 Hz power line frequency
  Computer  NTP
  Laser  RF reference via optical frequency comb
The most superior (accurate) clocks are localized in research / NMI laboratories and not very mobile (Cs fountain clocks)
However…
https://company.sbb.ch/de/ueber-die-sbb/profil/sbb-markenportal/basis/sbb-uhr.html
https://www.chrono24.de/magazine/james-bond-uhren-p_23000/
Copyright ESA-P. Carri
https://en.wikipedia.org/wiki/Network_Time_Protocol
National Metrology Institute
METAS, NIST, PTB etc.

## Slide 5: FoCS-2: Fontaine continue Suisse à jet de césium
Made in Switzerland
Rendez-vous Bundeshaus, 2014

## Slide 6: How to measure a frequency/time signal?
Compare it to a reference of equal or superior accuracy
  Mechanical watch  train station watch
  Radio clock  GPS / Radio signal
  Kitchen oven  50 Hz power line frequency
  Computer  NTP
  Laser  RF reference via optical frequency comb
The most superior (accurate) clocks are localized in research / NMI laboratories and not very mobile (Cs fountain clocks)
How to get the reference to the user?
Frequency dissemination
However…
National Metrology Institute
METAS, NIST, PTB etc.

## Slide 7: Frequency dissemination
Satellite techniques (GNSS, TWSTFT)
  Based on RF (1-12 GHz) frequencies
  Ultimate limit , reached after days
Mobile clocks
State-of-the-art

## Slide 8: Evolution of modern atomic clocks
F. Riehle, Comptes Rendus Physique, Volume 16, Issue 5, June 2015, Pages 506-515
https://doi.org/10.1016/j.crhy.2015.03.012
Cs Primary Frequency Standard
Optical clocks
Limit of satellite comparison

## Slide 9: Frequency dissemination
Satellite techniques (GNSS, TWSTFT)
  Based on RF (1-12 GHz) frequencies
  Ultimate limit , reached after days
Mobile clocks
Optical fiber networks
  Based on optical telecom (190 THz) frequencies
  Ultimate limit , reached after hours
  Requires active phase noise cancellation
  Necessity for state-of-the-art clock comparison
State-of-the-art
Emerged as the new state-of-the-art

## Slide 10: Time and frequency networks: Situation in Europe
                H. Schnatz: Towards a European fiber network, ESA ACES Workshop, Zürich, June 2017
Past and recent international projects
EMRP NEAT-FT
EMPIR OFTEN
EMPIR TiFOON
Horizon 2020 CLONETS (-DS)
…

## Slide 11: Example France
http://www.refimeve.fr/index.php/fr/presentation/com-allevents-settings/t-refimeve.html
Optical clock comparison

## Slide 12: Example Italy
Very long baseline interferometry (Medicina – Matera)
Galileo GNSS (Fucino)
Atomic and molecular spectroscopy (LENS, Firenze)
INRIM: http://rime.inrim.it/labafs/frequency-dissemination-through-optical-fibers/

## Slide 13
Cantin et al., New J. Phys. 23 (2021) 053027

## Slide 14: Network implementation
Dedicated (dark) fibers are difficult to obtain
Share fibers with existing data network
Profit from existing fiber network infrastructure
SWITCH has Points-of-Presence (PoPs), necessary for installation of network components (EDFA, OADM filter)
SWITCH fiber network backbone
What wavelength?
Fibers

## Slide 15: Spectral consideration: L-band vs. C-band
C-band
  Low attenuation, high amplification gain
  The ‘popular’ choice
  Used in existing frequency networks
  Heavily used for data traffic
  Not available in our network
L-band
  Mostly unused
  Spectrally separated from data traffic
  Not yet tested for our application
www.itu.int/ITU-T
EDFA spectrum
(amplification)

## Slide 16: Network implementation
Independent dark channel – but in the same fiber as data traffic!

## Slide 17: Network implementation
Independent dark channel – but in the same fiber as data traffic!
SWITCHlan backbone

## Slide 18: Swiss frequency metrology network: numbers
Item | Value
Operating wavelength | 1572.06 nm
ITU-T Channel | CH07
Total length | 456 km
# Segments | 3
# Bidir EDFA | 2 / 2 / 3
# Regeneration stations | 2 (Basel, Zurich)

## Slide 19: Environmental noise
Fibers act as microphones …
… picking up noise from environment (temperature, acoustic vibrations)
Causes variation of optical path length and thus phase
Distorts the stable frequency at the recipient end
 Requires phase noise read-out and compensation

## Slide 20: Phase noise cancellation
Frequency correction
1
2
1
2
Michelson-Interferometer
Phase error
FM
FM
Control loop
Frequency shifter
Local
Remote
X km
3
3

## Slide 21: Laboratory side: implementation
Ultrastable SI-traceable laser
Stabilized to cavity for narrow linewidth
Stabilized to frequency comb for absolute reference
Comb referenced to active maser
Maser is part of UTC(CH)
Maser is compared to TAI via UTC(CH)
>> SI-traceable
 SI-traceable
Bern

## Slide 22: Laboratory side: implementation
 SI-traceable
Phase noise cancellation
2 AOMs for frequency shifting and correcting
Bidirectional EDFAs for compensation of power losses
Regeneration laser
Offset locked to incoming signal
Used for local distribution
Sent downstream into next fiber segment
 Phase-noise compensated
Bern
Basel

## Slide 23: Laboratory side: implementation
 SI-traceable
 Phase-noise compensated
 Verified on round-trip signal
Zurich
Bern
Basel

## Slide 24: In-loop phase noise measured
Phase noise cancellation off
Phase noise cancellation on
160 MHz beat
Bern
Basel
Zurich

## Slide 25: Phase noise: end-to-end
Bern
Efficient noise suppression for frequencies < 100 Hz
Noise suppression of around 50 dB at 1 Hz
Limited by longest leg residual delay-unsuppressed noise
Basel
Zurich
Theoretical limit:

## Slide 26: Phase noise over time
Increased noise during daytime

## Slide 27: Long term stability: Allan deviation
Free-running link
MDEV
ADEV -averaged
Fractional frequency uncertainty

## Slide 28: SI-traceable measurement of a laser in a remote lab
Bern
Basel

## Slide 29: SI-traceable measurement of a laser in a remote lab
Light from METAS
Basel
Molecular spectroscopy lab
Measured against GPSD Rb clock
Measured against METAS frequency
un-steered
steered
Improvement of measurement uncertainty by two orders of magnitude!
Measured frequency uncertainty of a spectroscopy laser in Basel

## Slide 30: Are we disturbing the data traffic?
Network bit error rate
- No!
Monitor bit error rate in the fibers shared with our metrological frequency signal
Direction
Different channles (frequencies)
No change in bit error rate
Validation that multiplexing our metrology signal into fiber network shared with data traffic does not cause detrimental interference

## Slide 31: Conclusion and Outlook
Conclusion
      Demonstration of a phase-stabilized link for frequency dissemination in the telecom L-band, multiplexed into an optical fiber network carrying data traffic
      Link fractional frequency instability of in around 2’000 s
      Measurement instability of a remote laser improved by 2 orders of magnitude
Outlook
      Use improved frequency resolution to access novel regimes in precision spectroscopy of Rydberg and molecular ion experiments
      Scale the network within Switzerland, connect more research institutes and stakeholders
      Connect to neighboring metrology optical fiber links in Europe
      (inter-)national comparison of frequency standards
Husmann et al., Optics Express
Vol. 29, Issue 16, 24592-24605, 2021
https://doi.org/10.1364/OE.427921

## Slide 32: Applications of the metrological fiber network
Precision spectroscopy
Seismology
Relativistic geodesy
Time dissemination
Clock comparison
Grotti et al., Nature Physics
https://doi.org/10.1038/s41567-017-0042-3
http://seismo.ethz.ch
Sinhal et al. Science,
https://doi.org/10.1126/science.aaz9837
Marra et al., Science
https://www.science.org/doi/10.1126/science.aat4458

## Slide 33: The Swiss Metrology link team
Jacques Morel
Laurent-Guy Bernier
Dominik Husmann
Daniel Bertolo
Ernst Heiri
Konstantinos Chaloulos
Fabian Mauchle
Felix Kugler
Davide Calonico
Cecilia Clivati
Alberto Mura
Stefan Willitsch
Ziv Meir
Mudit Sinhal
Anatoly Johnson
Aleksandr Shlykov
Frédéric Merkt
Hansjürg Schmutz
Gloria Clausen
Simon Scheidegger
Urs Hollenstein
Jérôme Faist
Giacomo Scalari
Mathieu Bertrand

## Slide 34: Thank you very much for your attention!

## Slide 35: Monitoring error signal: a seismic probe?